## Slide 1: Introduction to Computer Science
Networks
Lecture e
This material (Comp 4 Unit 6) was developed by Oregon Health & Science University, funded by the Department of Health and Human Services, Office of the National Coordinator for Health Information Technology under Award Number 90WT0001.
This work is licensed under the Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License. To view a copy of this license, visit http://creativecommons.org/licenses/by-nc-sa/4.0/.
Notes: Welcome to Introduction to Computer Science: Networks. This is Lecture e.
The component, Introduction to Computer Science, provides a basic overview of computer architecture; data organization, representation, and structure; structure of programming languages; and networking and data communication. It also includes some basic terminology from the world of computing.

## Slide 2: Learning Objectives - 1
Define what a communication network is (Lecture a)
Explain the purposes and benefits of a communication network. (Lecture a)
Explain the Internet and World Wide Web, their histories, and their structures. (Lecture a)
Describe different ways of connecting to the Internet. (Lecture a)
Notes: The objectives for this unit on Networks are to:
Define what a communication network is,
Explain the purposes and benefits of a communication network,
Explain the Internet and World Wide Web, their histories, and their structures,
Describe different ways of connecting to the Internet,

## Slide 3: Learning Objectives - 2
Explain the basics of network addressing
  Internet Protocol (IP) addresses
  Domain names
  Lease vs. purchase from an Internet service provider (Lecture b)
Introduce network classification by the coverage size. (Lecture b)
Notes: Explain basics of network addressing: IP addresses and domain names, and how they can be leased or purchased from an Internet service provider.
Introduce network classification by the coverage size.

## Slide 4: Learning Objectives - 3
Describe different network topologies. (Lecture c)
Outline different standards and protocols that govern wired and wireless communications. (Lecture c)
Notes: Describe different network topologies.
Outline different standards and protocols that govern wired and wireless communications.

## Slide 5: Learning Objectives - 4
Describe benefits and disadvantages of wireless communication and a typical wireless network setup. (Lecture d)
Describe network hardware. (Lecture d)
Introduce networking logical models and discuss Open Systems Interconnection (OSI) model. (Lecture e)
Notes: Describe benefits and disadvantages of wireless communication and a typical wireless network setup.
Describe network hardware.
And, finally, to introduce networking logical models and discuss Open Systems Interconnection, or OSI model.

## Slide 6: Networking Logical Models
Devices and software mapped to logical model to use OS functionality
  OS programs load when computer boots
  OS services are applications that are always running in the background
Composed of a series of layers that defines specific functionality
OSI (Open Systems Interconnection) model defines how network hardware and software operate
Notes: This lecture will explain the OSI networking model that future programmers and database experts need to understand, along with specific functionality for specific devices or software.
When hardware and software are created, the engineers need to understand how the devices and software are going to be programmed. The operating system follows a logical model that facilitates communication between hardware and software. A logical model is composed of a series of logical layers that define specific functionality for a device or for a piece of software. The open systems interconnections, or OSI, model defines how network hardware and software operate.

## Slide 7: The OSI Model
Seven logical layers
  Application (7), Presentation (6), Session (5), Transport (4), Network (3), Data Link (2), Physical (1)
Each layer’s communication is standardized
Device and software communication is standardized using OS services
Example: Email
Notes: The OSI model is composed of seven logical layers.
The top layer, layer seven, is the Application, followed by the layers Presentation, Session, Transport, Network, Data Link, and Physical. The Physical layer is always layer one and the Application layer is always layer 7.
Each layer's communication is standardized so that adjacent layers know how to communicate with each other. In other words, layer seven has the ability to communicate with layer six. Likewise, layer six has the ability to communicate with layer five AND layer seven. Layer five can communicate with layer four and layer six, and so on.
Therefore, device and software communication is standardized by operating system services. Remember that a service is simply a program that starts when the operating system loads. When a computer boots, the boot process loads a number of operating system services.
Depending on the device and/or software, one service calls on the functionality of another service to facilitate network functionality and communication.
To understand how hardware and software use operating system services let’s look at the example of creating and sending an email message.
First, you open the email application. Then you start a new message. You type what you want to say, and you send the email.
The email application needs operating system services to take the email from what is seen on the screen and make it in to an electronic equivalent that can be sent out via the computer's network interface card, or NIC. Many operating system services work together to accomplish this task.
Services operate within specific OSI logical layers. One service can operate in many layers, depending on what it is doing at any moment in time. Services call on each other as the email works its way towards the NIC via the motherboard circuitry. The NIC calls on services to encode the email for transport out of its port or over the air through an antenna. Then, when the next device, such as a switch or router or even an email server, receives the email electronically, the receiving device uses its hardware and services to process the email.
The next few slides will examine each of the layers of the OSI model in a little more detail.

## Slide 8: OSI Model Layer 7: Application Layer
Software calls on OS services to begin the network communication process
  You click “send” on an e-mail to start this process
  The communication is called data at this level
  Web browser uses same process
  No devices operate at this layer
Notes: In the OSI model, layer seven is known as the Application layer. Software installed in a device calls on the OS services to begin the network communication process by converting the software's communication into a format that can be readied for transmission. For example, clicking Send in our email example starts this process. Note that the communication is data at this level.
A web browser, or any network-enabled program, goes through the same process every time a user visits a web page. This is the same process that a smart phone uses to operate.
No devices operate at layer seven, because this is where software works on behalf of hardware. Layer seven is closest to the user, so this is where email is originated. However, if the example centered on the user’s computer receiving an email, the discussion would begin at layer one, which is where the NIC receives electronic signals.

## Slide 9: OSI Model Layer 6: Presentation Layer
Takes the converted message and further transforms it for electronic transmission
Also handles file compression and/or encryption if the file is or needs to be encrypted
  If your e-mail a compressed file, the compression type used, etc. is handled here
  The communication is still called data at this level
Notes: OSI model layer six is the Presentation layer. No devices operate at layer six because this is where software works on behalf of hardware, just like layer seven. At layer six, the converted message received from layer seven is further transformed for electronic transmission.
Layer six also handles file compression and encryption when needed. If a user emails a compressed file, the compression type, for example ZIP, is handled here. Note that the communication is still called data at this level.

## Slide 10: OSI Model Layer 5: Session Layer
Manages asynchronous application-to-application communication
  You send an e-mail to your friend. Services here record that an e-mail program needs to receive this communication (and vice-versa).
  The communication is still called data at this level
Notes: At OSI model layer five, the Session layer manages asynchronous application-to-application communication.
When you send an email message, services at this layer record that an email program needs to receive this communication. Note that the communication is still called data at this level.
The term “asynchronous” means that the sender and the receiver do not need to communicate at the same time.
No devices operate at layer five because again, this is where software works on behalf of hardware, just like the Application and Presentation layers. Again, the communication is still called data at this level.

## Slide 11: OSI Model Layer 4: Transport Layer
TCP and UDP protocols
Manages asynchronous device-to-device communication
  Sending email
  Receiving email
Ensures communication pieces are in right order
Segment encoded about communication and instruction
Notes: OSI model layer four is the Transport layer.
As in the Application, Presentation, and Session layers, no devices operate at layer four because this is still where software works on behalf of hardware. The transmission control protocol, or TCP, suite of protocols operate at this layer, as does the user datagram protocol, or UDP.
The Transport layer manages asynchronous device-to-device communication. For example, when sending an email, services here indicate where a file and the actual communication begin. When receiving an email, the services also indicate where a file ends, and when the communication process should be considered complete.
It also ensures that pieces of the communication are put in the right order, whether sending or receiving communication.
At the Transport layer, the communication is a segment, encoded with information about the communication and instructions.

## Slide 12: OSI Model Layer 3: Network Layer
Manages asynchronous network-to-network communication
Router: Device that operates at this level
Splits segments into packets
Prepare packet by adding information
  Header: Source and IP address
  Footer: Damage to packet
Router uses IP to route packets
Notes: Next is OSI model layer three, known as the Network layer. This layer manages asynchronous network-to-network communication. Services split the segment into manageable sizes called packets and then further encode each packet with information used by layer three devices. A router is an example of a device that operates at layer three.
Services prepare the packet for traffic by adding to each packet electronic pieces of information, including a header and footer. Information stored in the header includes the source and destination IP address. The footer contains the result of a mathematical calculation that helps devices determine damage to the packet.
Services inform receiving devices about the packet's source, its destination, protocol, and more. The Internet protocol, or IP, operates at this layer. Routers use IP addressing to route packets to their final destination.
TCP does not operate at this level. It becomes operable in layer four, the Transport layer.
Finally, at the Network layer of the OSI model, the communication is a packet.

## Slide 13: OSI Model Layer 2: Data Link Layer
Determines applicable networking protocols for packet
Readies packet for transport using technology supported by the NIC
Uses copper cable; expects IEEE 802.3
Switches and NICs operate here
Communication is called a frame
  Includes all communication from pervious layers
  Encapsulated by header and footer
Notes: OSI model layer two, the Data Link layer, determines applicable networking protocols for this packet. At the same time, layer two services ready the packet for transport using whatever technology the NIC supports. Examples include Ethernet, wireless, fiber-optic, or a combination of these technologies.
The computer's NIC may use copper cable and expects a communication encoded according to the Ethernet standard, the IEEE 802.3 standard.
Switches and NICs are examples of devices that operate at layer two. Therefore, media access control, or MAC, addressing applies, and MAC addresses are used for communications between layer two devices.
Note that the communication is a frame at this level. The frame includes all of the communication received from layers seven through three and is encapsulated by a header and footer.

## Slide 14: OSI Model Layer 1: Physical Layer
NIC takes digital electronic signal and transforms it
  E-mail Example
Devices used at this level
  Hubs
  NICs
  Cables
  Antennas
Communication is called bits at this level
Notes: At OSI model layer one, known as the Physical layer, the NIC takes the computer's digital electronic signal and transforms it into a signal that can be put on the NIC's media. Therefore, an email translates into electronic impulses and moves from the NIC to the wires at the end of the RJ45 connector, which is at the end of a network cable. The electronic impulses are bits, or binary digits. The bits transmit across the entire cable length to the next device, which is usually a switch or router.
Hubs, NICs, cables, and antennas are examples of devices that operate at layer one. NICs operate in both layers one and two of the OSI layer, but primarily at layer two.
Finally, note that the communication at layer one is a bit.

## Slide 15: Acronyms Help to Memorize Layer Order
Review of layers
  Application (7), Presentation (6), Session (5), Transport (4), Network (3), Data Link (2), Physical (1)
  Top to Bottom:
    All People Studying This Need Dr. Pepper
  Bottom to Top:
    Programmers Do Not Throw Sausage Pizza Away
Notes: At this point, the OSI model, its layers, and the functionality that occurs at each layer may seem overwhelming. Fortunately, there is a way to help memorize the layer order of the OSI model.
Here is a mnemonic to help remember the seven layers from top to bottom:
All People Studying This Need Dr. Pepper
Or, if you prefer, from bottom to top:
Programmers Do Not Throw Sausage Pizza Away
Take some time for review to remember each of the layers of the OSI model, and perhaps construct a one-sentence explanation about the functionality of each layer.
Anyone who plans to work with routers, switches, or servers will most likely need to know more about the OSI model and its services. A deeper understanding of the OSI model is beyond the scope of this discussion.

## Slide 16: Devices and the OSI Model
Devices operate at specific layers
  Layer 3: Routers and switches that also function as a router (known as a “L3 switch”)
  Layer 2: Switches and most NIC functionality
  Layer 1: Hubs, some NIC functionality, network cabling, wireless antennae
Notes: As discussed earlier, the OSI model shows that certain devices operate at specific layers. To review, at layer three, routers and switches that function as routers. Such a switch is a layer three switch.
Layer two has switches and most NIC functionality.
Layer one has hubs, some NIC functionality, network cabling, and then wireless antennae.

## Slide 17: OSI Model and the Medical World - 1
Concepts are found throughout networking and programming
Medical software and devices send network traffic adhering to a standard known as HL7
Example – EKG
  Image transmitted to EHR
  Information encoded according to the rules in OSI model
Notes: Why learn about the OSI model? Future programmers and database experts will need to understand how things happen electronically.
In fact, concepts related to the OSI model are found throughout networking and programming. Many medical software applications send network traffic adhering to a standard known as Health Level 7, or HL7, named after the OSI model layer seven.
An example is an EKG image being transmitted from a machine to the patient's electronic health record, or EHR, encoded in accordance with HL7 rules. In this transaction, the receiving EHR database is informed of the type of image received, the patient record number, equipment identification, supervising clinician, and so on. The information is encoded in this communication, according to the rules discussed in the OSI model.

## Slide 18: OSI Model and the Medical World - 2
EHR database software contains the HL7 encoding rules and is able to understand and act on the communication
  EHR program uses OS services just like any other network-enabled installed software
Note: other medical encoding standards exist
Notes: In addition, EHR database software contains HL7 encoding rules and is able to understand and act on the communication received from the EKG machine. Therefore, the EHR program uses operating system services just like any other network-enabled software.

## Slide 19: Networks Summary - Lecture e
Discussed OSI networking model
  Explained specific functionality for device or software
Notes: This concludes lecture e of the unit on Networks. In summary, this lecture covered the OSI networking model that future programmers and database experts will need to understand. It also discussed specific functionality for specific devices or software.

## Slide 20: Networks – Summary
Communication network
History of Internet and World Wide Web
Network connections
  Wired
  Wireless
Network topologies
OSI model
Notes: That also concludes the unit on Networks.
To review, in this unit we explored the concept of a communication network, examined the history of the Internet and World Wide Web, investigated both wired and wireless network connections, identified various network topologies, and introduced the open systems interconnection model.

## Slide 21: Networks References – Lecture e
References
Wikipedia. [Internet]. 2011 Nov [cited 2011 Nov 07]. Available from: http://en.wikipedia.org/wiki/OSI_model.
Notes: References slide. No audio.

## Slide 22: Introduction to Computer Science Networks Lecture e
This material was developed by Oregon Health & Science University, funded by the Department of Health and Human Services, Office of the National Coordinator for Health Information Technology under Award Number 90WT0001.
Notes: No audio.